## Connecting to WiFi - GRP2614, GRP2615, GRP2616
To connect the these models to a WiFi Network, please follow the steps below:
1. From the Home Screen, press the Round button between the 4 arrow buttons, and navigate to System → WiFi settings.
Fig. 81: WiFi Feature
2. Set WiFi to Enabled and press Save button.
Fig. 82: Enabling Wifi
3. Select Scan. The device will automatically start scanning for WiFi access points within range.
Fig 83: WiFi Scanning
4. A list of available WiFi networks will be displayed. Select the desired network.
Fig 84: Nearby WiFi networks
5. If required, enter the WiFi network password to connect.
Fig 85: WiFi password required
6. An incorrect password will trigger the error message Cannot connect to the selected network. - If the connection is successful a “WiFi Network Connected” message will display on screen
Fig 86: Failed/Successful WiFi Connection
7. Check the WiFi icon on the Home Screen to verify if the WiFi network is properly connected.
Fig 87: WiFi Status
8. A new section Current Connection will show under System → WiFi settings.
Fig 88 : Current Connection
9. Selecting Scan, users may choose to Forget the current connection and establish a new one.