## Headsets - Wired and Bluetooth
### Wired
The GRP2614,GRP2615, & GRP2616 phones support normal RJ11 headset and Plantronics EHS headsets. To use a Plantronics EHS headset:
1. Go to the Phone Menu > Preferences > Audio Control: Headset Type.
2. Select Plantronics EHS then reboot the phone.
3. Connect Plantronics EHS Headset into the RJ11 headset port on the back of the phone.
4. To use headset mode, press headset button . A headset icon will show on the LCD.

Headset Mode Enabled
### Bluetooth
GRP2614,GRP2615, & GRP2616 phones also connect to Bluetooth headsets (Bluetooth version 5).
To connect to a Bluetooth device, turn on the Bluetooth radio first. The first time using a new Bluetooth device, it will have to be paired with the phone so that both devices know how to connect securely to each other. After that, the devices will simply connect. Bluetooth related settings are found at Phone Menu → System → Bluetooth.
Bluetooth Discoverable
There are two ways to pair the GRP2614/GRP2615/GRP2616 using the Bluetooth feature:
I. From the GRP261X
1.Select Start Scan to search nearby Bluetooth devices.

Bluetooth Scan
2. Choose a device then select Pair. The phone will then start the pairing process.
Bluetooth Pairing
3. If the pairing succeeds, Connected will display next to the name of the Bluetooth device.
II. From the Bluetooth Device